## Slide 1
LIGHTS ON PARKING

## Slide 2
The Problem
In huge city is very difficult looking for a parking space near your home, your work place o wherever you prefer to go.
Citizens search for much time a parking lot and so they are stressed and tired.
Researches:
INRIX research (link)
IBM research (link)

## Slide 3: What are the problems?
Human stress
Ambiental pollution
Traffic
Useless expense

## Slide 4
Rome parking situation
From the research of Parkclick.it we found the following data:
35-45 minutes a day (4 hours a week);
7/10 Romans use the car to go to work;
  2/3 park on the street;
629 cars for every 1000 citizens;
107 hours a year in the traffic.

## Slide 5: Our solution
Lights on Parking is a project created to monitor the availability of parking spaces and consequently, if they are free, indicate them to the citizen through an app / web page, optimizing the traffic of those looking for a lot.

## Slide 6: Goals
A smart way to find a parking space efficiently
Less time spent in the car
Less stress for the drivers
Reduction of traffic due to the search for a parking space
Reduction of fuel consumption(economic aspect)
Reduction of fuel emission (ambiental aspect)

## Slide 7: Requirements
1.Space: parking lots
2.Information: availability or occupancy
3.Individual: citiziens
4.Time: real time
5.Energy consumptions: lower possible

## Slide 8
THE DEVICE

## Slide 9
Pros and cons
We have analyzed the requirements and we have choosen for our project the sensor over the asphalt with coverage.

## Slide 10: The prototype

## Slide 11
STMICROELETRONICS B-L072Z-LRWAN1 STM32 LoRaWAN DISCOVERY BOARD:
is a development tool to learn and develop solutions based on LoRa.
HC-SR04:
an ultrasonic sensor uses sonar to determine distance to an object.

## Slide 12
Hardware Schema
The project is built in a STM32 LoRaWAN Discovery board, in which we implemented an ultrasonic proximity sensor which is used to determine when a car is parked in a certain parking space.

## Slide 13
Software Schema

## Slide 14: Web Page

## Slide 15
The code
The device measures by means of the ultrasonic sensor the distance from the car and there are two cases:
  There is a car → the parking lot is occupied.
  There is nothing → the parking lot is free.
The update of the data in the cloud is done only when there is a change of the state.

## Slide 16
The demo
The demo is available here:
https://www.youtube.com/watch?v=2jt28GkLYO0&t=4s

## Slide 17
EVALUATION

## Slide 18: Our assumptions
Website link

## Slide 19
Energy consumption
We have analyzed energy consumption trying to reduce it efficently.
Our measurements change according to the states of parking spaces.
The states are:
Free: data measure every 30 seconds;
Occupied: data measure every 10 minutes.

## Slide 20
Device Consumptions
Battery: 14000mAh power bank
Ultrasonic sensor consumes 15mAh
Board STM32 consumes:
  12.7mAh in run mode
  0.82mAh in sleep mode

## Slide 21
Three specific evaluation cases

## Slide 22
Constantly connected device
In 1 hour it consumes (15 + 12.7) mA = 27.7mAh
In one day it consumes 664.8mAh
The device discharges after approximately 21 days.

## Slide 23
Device with always free parking (worst case)
We check parking situation every 30 seconds.
58s sleep mode. -> 3480s of sleep mode -> consumes 0.79mA in one hour.
2s run mode. -> 120s of run mode -> consumes 0.42mA in one hour
Overall in 1 hour it consumes (0.79 + 0.42) mA = 1.21mA.
In one day it consumes 29.04mA.
The device discharges after approximately 482 days.

## Slide 24
Device with always occupied parking (best case)
We check parking situation every 10 minutes.
3594s of sleep mode in 1 hour -> consumes 0.818mA in one hour
6s of run mode in 1 hour -> consumes 0.046mA in one hour
Overall in 1 hour it consumes (0.818 + 0.046) mA = 0.864mA
In one day it consumes 20.736mA.
The device discharges after approximately 675 days.

## Slide 25: Radio usage
Sending data only:
Empty parking space -> Occupied parking space.
Occupied parking space -> Empty parking space.

## Slide 26: Latency
TUltrasonic+TMessage+TAir+TCloud = 1s+0.05s+0.08s+2s≃3s
TUltrasonic = 1s
TAir = 0.05s
TAir = 0.07s - 0.08s.
TCloud = 2s

## Slide 27
Future plans
-Electromagnetic sensor
-Edge computing

## Slide 28
THANKS FOR WATCHING!